## Slide 1: Sportsfields Irrigation Management In Ipswich
Geoff Faulkner
David Baker
PLA Conference
Darwin 2009
Notes: There can be no doubt in anyone’s mind that water, especially town water, has become a valuable commodity to be managed for best use.
Supply is diminishing and demand is increasing and the water footprint of products and commodities is being developed to aid consumers in making a green choice.
Much has been done in the areas of education, incentives and regulation to help reduce the impact of the shortfall of demand over supply.

## Slide 2: Introduction
ICC has an area of 1,089 sq km and a population of 160,000 in SEQ, west of Brisbane.
500 Parks and Reserves
Council manages 33 ha of irrigated sportsfields
Notes: I’d like to start the presentation with a little information about Ipswich to set the context.
Ipswich is just west of Brisbane in south-east Queensland with a population of 160,000.
Even though the CBD is just 50 km from the coast, its average rainfall of 847mm is only 70% of Brisbane’s rainfall. In addition, it has higher average maximum and lower average minimum temperatures and evaporation levels are also higher.
Council has some 500 parks and reserves and actively manages 33ha of irrigated sports fields.

## Slide 3: Overview
Management pre drought
Journey through regulation and philosophy
What we did and how it worked
Where we are at now
Notes: What I will be presenting today is a brief background to Council sports field management and how Council responded to the challenges of a developing regulatory framework.
I will outline how fields were traditionally irrigated prior to regulation; our journey through regulation; our driving philosophy, responses and initiatives, and our current situation.

## Slide 4: Pre 2005
Subjective irrigation management
Poor understanding of water consumption
320 ML used in Parks and Sportfields in 2005
Notes: It is fair to say that irrigation consumption was not a principal consideration prior to 2005.
If an irrigation system was installed then it was used to present a quality turf playing surface.
Irrigation management was at the discretion of the field supervisor in line with other agronomic management decisions such as fertiliser, aeration, etc.
Irrigation systems were generally pop-up sprinklers connected to a controller which were manually programmed to irrigate at pre-determined scheduled times. Some rain clicks were installed at some locations.
A plethora of water meters, connection sizes and mixed use prevailed eg. In some situations, a single water meter may have been used for water used for irrigation of sportsfields, garden beds,
Clubhouse use etc. In other cases, there could be ten or more meters for some of the larger parks and sportsgrounds.
Water consumption was rising annually as more irrigation systems were installed to a total of 320ML in the 2004-05 year.

## Slide 5: 2005 and Beyond
Town water use regulated by the Qld Water Commission (QWC)
Spotlight on water use and management
  Data collection and analysis
  Alternative source investigations
  Combination of WEMPs and APS depending on use and restriction level.
Notes: The state government regulated town water use in for south-east Queensland 2005. This put the spotlight on business and domestic water consumption practices.
Water Efficiency Management Plans were required for high volume users and had to comply with a number of guidelines for water use.
Two initial key components for sports fields were the need to install sub-meters to separate ‘inside’ water from ‘outside’ water and the times at which irrigation could take place.
In an effort to reduce our town water use for irrigation, we investigated alternate sources such as surface storages, bore water, and tidal river water. Due to water quality and sustainability issues result in these water sources being opportunistic and part of the answer but are unlikely to entirely replace the reliance on town supplies.

## Slide 6: SEQ Restrictions
  Changing Targets:
  Level 1 May 2005
  Level 2 October 2005
  Level 3 June 2006
  Level 4 Nov 2006
  Level 5 April 2007
  Level 6 Nov 2007
  High July 2008
  Medium April 2009
Notes: As the restriction level changed, so did the guidelines. There have been 8 restriction changes in the last 4 years.
Level 6 restrictions in November 2007 saw the introduction of the ‘Active Playing Surface’ guidelines.

## Slide 7: How much water to use?
Two philosophies:
Volumetric allocation
  easy to regulate
Soil Moisture Needs Based
  Needs data
Notes: There was much discussion between stakeholders and the QWC in the lead up to the APS guidelines. All agreed that sports fields contributed to the social fabric, however irrigation needed to be kept to a minimum.
Ipswich championed the philosophy of being able to irrigate with just enough water to meet a deficit in available soil moisture that would be required for the fields to be in a ‘fit for play’ condition.
The other philosophy was to make a monthly volumetric allocation.
The volumetric allocation can either be an arbitrary figure based on a notional reduction in use. Eg. Reduction of 25% use over the previous year or based on assumptions of expected rainfall.
Council had been collecting soil moisture data using a manual gauge and relating the result to level of stress in the turf. While the soil moisture probe gave us the soil moisture, it was apparent that the available soil moisture varied according to soil type. We decided that, in the absence of sufficient data across soil types, we would use a reading of 15% as the trigger to commence irrigation based on our collected data.
The next step was to determine how much water to apply to bring the turf out of stress but not so much as to fill the profile to field capacity. We developed a calculator based on standard irrigation formulas to bring the profile to 75% of field capacity.
This calculator was adapted by the QWC to develop the adopted volumetric allocation allowable. The rainfall data in the QWC calculator is based on historical rainfall.

## Slide 8: Volumetric Allocation
Pros
Easy to regulate and audit for compliance.
Low training requirement.
Cons
Calculation for the allocation based on historical daily rainfall
Allocation is likely to be inadequate in drought
Does not account for prevailing rainfall
Notes: The Volumetric Allocation is easy to regulate because a known amount of water will be applied and staff training requirements are low.
The major problem is that the allocation may be less than what is needed for the turf if the expected rainfall doesn’t eventuate or it may be too much if rainfall is greater that assumed. Either way, the water is not used effectively. In other words, too little or too much water is wasted water.

## Slide 9: Soil Moisture Needs based
Pros
Can provide turf in a ‘fit for play’ condition with the minimum of amount of water.
Cons
Requires understanding of soil profile features – texture, depth, WP, FC
Requires tools to measure regularly
Requires knowledge of irrigation system
Notes: Irrigating according to soil moisture means that the actual immediate water requirement of the turf is met. Our aim is a ‘fit for play’ surface.
There are two major steps in the process:-
1. Decision making; when to intervene with irrigation and how much to apply; and
Efficient and responsive irrigation systems to act on the decisions.
Decision making requires a good agronomic understanding and data collection tools.
Irrigation management systems need to be efficient, responsive and easily manipulated.
Staff training for both steps is paramount.

## Slide 10: ICC Irrigation Principles
Irrigation to overcome a deficit in available soil moisture required for turf growth
  Turf condition for ‘local’ sport = ‘fit for play’
System management
  Efficient & effective irrigation practices and systems
  Agronomic measures; eg turf selection, nutrients, verti-draining, soil ameliorants etc.
Notes: An over-riding principle is that water will not fix all problems. More water will not cover for soil profile, turf selection, nutrients, and compaction problems.
A ‘Fit for Play’ surface is when conditions are within safe limits for play.
A key standard is the surface hardness test and is measured by a Clegg Impact Soil Tester. This measures the gravity of deceleration applied when the weight hits the surface. Our playing surfaces are regularly monitored for hardness.
Hardness varies with vertical thickness of grass and soil moisture.

## Slide 11: What We Did
Data collection & analysis
  water consumption
  Alternative supply
  Surface hardness, compaction, moisture
Determined ‘fit for play’
Identified and installed information and management systems
Developed management processes
Adaptive management
Notes: Decisions need to be based on data. We commenced reading the water meters weekly, commenced monitoring soil moisture and installed an integrated central control irrigation system so that we could efficiently alter run times and programmes.
Our system operates on adaptive management and continual improvement based on ongoing data collection and responses because data on soil moisture requirements for sports fields is not readily available and not all sports have safety ‘hardness’ standards.
The manual soil moisture probe gave us some valuable insight but is time consuming.
Now convinced that this process is worthwhile, we commenced installing permanent soil moisture probes. It is important to locate the probes in the most representative part of the field.
The system we chose is web based that enables real time data access and parameter manipulation while logged on to the internet. The system allows us to set low and high points for soil moisture and, in automatic mode, over-rides the irrigation control until soil moisture decreases to the low set point. Irrigation is then enabled at scheduled times until the high set point is reached when the system then disables the irrigation. Rain switches ensure that irrigation is suspended if it rains during an irrigation cycle.
The data we captured initially was soil moisture at root zone and at 30cm, temperature at root zone, and flow. We now capture soil moisture, soil temperature, and electrical conductivity at increments to 40cm as well as flow and rainfall.
The centrally controlled irrigation system then allows us to ‘fine tune’ the irrigation scheduling based on the physical data without the need to drive out to the field to manually set the programming.

## Slide 12: Some System Components
Notes: Some examples of the equipment are rain bucket, rain switch, integrated irrigation controller, soil moisture sensors, and software.

## Slide 13: Web Graph
Notes: This graph shows data of a typical cycle for a field showing soil moisture decreasing (blue line) and the system enabling irrigation (black line) when the low set point is reached. Irrigation (blue bars) and rain (red tag) then puts the soil moisture above the high set point and irrigation is again disabled and so on.
Note that rain at the end of the irrigation cycle sent soil moisture to field capacity.

## Slide 14: Annual Consumption 2005 - 2009
Notes: Using 2005 as a base line, you will notice that the consumption starts to decrease from 2007 but coincides with an increase in rainfall. This shows the responsiveness of using soil moisture rather than an arbitrary allocation value based on a predicted rainfall pattern.
If using the allocation method and given the higher than expected rainfall, would field managers have used less water than that allocated? No-one can answer that with assurance. Human nature being what it is may suggest the allocation would have been used no matter what!
Had the rainfall not been as high, then we would have used more water. Would it have been higher than the allocation? It may well have been. The question then becomes, ‘Would the allocation have been sufficient to provide a surface ‘fit for play’?

## Slide 15: Case Study Comparison
Results graph
Notes: This graph shows a case study of monthly comparisons between allocated volume and actual irrigation as determined by soil moisture for two soccer fields totalling 16,500 m2. Note the monthly variance. Actual soil moisture driven consumption was 4311 kL while the allocation we could have used 5534 kL.

## Slide 16: Cost Comparison
For the 2008/09 year
Using QWC Allocation, could have used 329L/m2.
33ha @ 329 L/m2 = 108.57ML @ $1750 = $190,000
Actual usage was 129L/m2.
33ha @ 129L/m2 = 42.57ML @ $1750 = $74,500
Saving of $115,500
Notes: The cost difference between monthly allocation and actual irrigation as determined by soil moisture translates to $115,500 over the 33 ha for the 2009 year.
As stated earlier, this may not have been the case had the rainfall been significantly less. What we do know is that the minimum volume of irrigation was used for the fields to be fit for play.

## Slide 17: Key points
Not just drought management
Efficiency demonstrates stewardship
Saves money
Better control
Notes: In conclusion, the key points from our journey are that, while the drought may have put the spotlight on our water consumption and usage patterns, we are confident that we are learning to use water efficiently and for a defined outcome.
While we can expect water restrictions will be a permanent feature, we now have the capacity to know the field conditions and when to intervene with irrigation. We can fine tune the applications as required without going to each field. We have the flexibility of adapting systems for both long term and short term needs.
We can demonstrate stewardship to the wider community that we are using water wisely.
This year we saved money.

## Slide 18: END
Thankyou.
Questions?